## Slide 1
Intro to NeoMatrix
Week 3 Exercises

## Slide 2: Building and Programming robots in TINKERCAD
This week you be continuing to program the NeoMatrix through TinkerCAD. This workshop aims to develop your text programming skills.
You should have completed silver from Week 2 before starting these challenges.
Please complete the bronze before starting the silver, and complete the silver before starting the gold.

## Slide 3: Neopixel and GFX APIs
NeoPixel: https://adafruit.github.io/Adafruit_NeoPixel/html/class_adafruit___neo_pixel.html
GFX API: http://adafruit.github.io/Adafruit-GFX-Library/html/class_adafruit___g_f_x.html#a59178a0e0c845a14a39b457c43567dd9

## Slide 4
Aims:
Animate one or more of the pictures from Week 2 silver to move across the neomatrix from left to right
  Remember to clear the screen between each step
  Start with the picture just off the left edge, e.g. -4
  Step through the x position until width is reached
Additional challenges:
  Add a ‘bounce back’ so that when it reaches the right edge, it then returns to the left
  Add vertical movement to the animated picture to have it ‘bounce’ off the top and bottom as it moves from left to right
BRONZE Challenge:

## Slide 5
Aims:
Draw text characters on the screen using the function:
matrix.drawChar (x, y, character, color, backgroundColor, size);
  You should draw characters at (0,0) and (6,0), e.g. ‘a’ and ‘b’
  One should have a background colour specified, the other can use 0 to leave the background blank
  size=1
Additional challenges:
Use the randomColor() from week 1 or nextRainbow() from week 2 to set colours
  For the rainbow, you may wish to give a larger increment value to see the change
Have a single character move from right to left of the display
SILVER Challenge:

## Slide 6
Steps:
Add a function to scroll messages across the display
  Remember to set the text colour before trying to display any messages
Additional challenges:
  Add a default parameter to set the background colour for drawing the message
GOLD Challenge:

## Slide 7
Extension Challenge:
What else can you add to this program?
Produce a series of animations that combine drawing pictures, colour patterns and scrolling text

## Slide 8
Thank You