## Slide 1: Arduino circuits

## Slide 2: Ardunios
This week, we’ll be using the Arduino to build and program some circuits

## Slide 3: BRONZE Challenge:
Step 1:
  Build a circuit using
    an Arduino
    a breadboard
    a resistor and
    an LED
  Connect the +ve on the breadboard to 5V on the Arduino
  Have the LED always on when the simulation is running

## Slide 4: BRONZE Challenge:
Step 2:
  Using the breadboard, connect another LED with resistor to pin 2 on the Arduino
  In the program:
    Delete the existing code in the forever loop
    Add the code to make the new LED turn on and off every second (wait 500 ms)

## Slide 5: SILVER Challenge:
Step 1:
  Add two more LEDs (and resistors) to your breadboard
  Connect the LEDs to pins 4 and 7 on the Arduino so you can program them

## Slide 6: SILVER Challenge:
Step 2:
  In your program, create a variable called “myNum”
  Inside your forever loop, set the variable to use the Math command to pick a random number between 0 and 3
  Using the Output command, print the myNum variable to the serial monitor
  Using the if-then-else blocks from the Control menu, turn on the number of LEDs to match the random number generated
    Note, you will need to “nest” these in the else-blocks (or switch to text-only mode
  Remember to add a wait block to slow down the loop so you can see the LEDs changing

## Slide 7: GOLD Challenge:
In a new Circuit, step 1:
  Add an LDR (photo resistor) and use a breadboard to connect it to an Arduino
  Create a variable and set it to the analog reading from the LDR
  Print out the values from the variable to the Serial monitor
What is the range of values generated by the LDR?

## Slide 8: GOLD Challenge:
Step 2:
  Add an LED to your breadboard and connect it to your Arduino
  Turn the LED on when the LDR reading is less than the middle of its range

## Slide 9: Extension Challenge 1
Create a new circuit that takes input from a temperature sensor
  Measure the range of values for the temperature sensor
  Add three LEDs so you have a blue, white and red LED
  If the temp < 0°C turn on the Blue LED
  else if the temp < 35°C turn on the White LED
  else turn on the Red LED

## Slide 10: Extension Challenge 2
Modifying the circuit with the LDR
  Change the LED to connect to a pin with a “~” in front of the number
  Instead of simply turning the LED on / off, try setting the output to the pin to be a number between 0 and 255. Try different numbers to see what happens
    255 is equivalent to “HIGH”, whilst 0 equates to “LOW”. This is a different range of values to that from the LDR
  Using the Math map function, try taking the LDR value and setting the brightness of the LED
    Note, you will need to switch to Text-Only mode to set the correct range for the LDR